|  | INTERNATIONAL AMATEUR RADIO UNION REGION 3 Thirteenth Regional Conference |  |
| --- | --- | --- |

August 7 - 11, 2006	Bangalore, India

Document No. 06/XIII/009

Agenda Items: 10.2.3, 11.8

Past 3 years of EMC Activities in the IEC/CISPR 
and amateur radio interference                                                                       IEC/IARU R3-XXX

Report from the IARU Region 3 EMC Coordinator, Dr. J. G. Rhee,

August 7, 2006

EMC matters may be discussed in the following international meetings, CIGRE, EBU, ETSI, ICAO, EURELECTRIC, ITU-R, ITU-T, UIC, UIE,  UITP, etc.

Among those, IEC/CISPR is the specialized organization which handles EMC matters primarily.

This report is based on the past 3 years of CISPR meetings including the latest one held at Cape Town, South Africa, from October 17th  to 21st  2005. The 69th IEC General Meeting as well as TC meetings were also held during the same period. 2004 CISPR meeting was held in Shanghai, China, and 2003 one in Seoul, Korea.

There were hundreds of participants from many countries from all over the world as well as from many organizations.

During the meeting period, the following sub committees were held, SC-A, B, D, F, H, I, & S.

SC-A: Radio-Interference Measurement and Statistical Methods

SC-B : Interference Relating to Industrial, Scientific and Medical Radio-frequency Apparatus, to other (Heavy) Industrial Equipment, to Overhead Power lines, to High Voltage Equipment and to Electric Traction)

SC-D : Electromagnetic Disturbances related to Electric/Electronic Equipment on Vehicles and Internal Combustion Engine Powered Devices.

SC-F : Interference relating to Household Appliances, Tools, Lighting Equipment and Similar Apparatus.

SC-H : Limits for the Protection of Radio Services

SC-I : Electromagnetic Compatibility of Information Technology Equipment, Multimedia Equipment and Receivers

SC-S : Steering Committee of CISPR

Among many TCs(Technical Committees), TC 77 is related to Electromagnetic Compatibility.

SC 77A : Low Frequency Phenomena                                                                                          SC 77B : High Frequency Phenomena                                                                                                SC 77C : High Power Transient Phenomena

Since the last TC-77 meeting was held in 2005 in Cape Town, the next one will be held in 2007.

1. For the amateur matters, PLC(Power Line Communications) issues may be one of the concerned subject, and the details are in the CISPR 22 Amd. 2 f9.

Amendment to CISPR 22: Clarification of its application to telecommunication system on the method of disturbance measurement at ports used for PLC (Power Line Communication)

As the speed of the PLC related devices are increasing near to the HF amateur band, argument on the possible interferences on HF receivers became a big issue. It is noticed that starting from the last year, many responsible experts start to admit the fact that PLC devices interfere to the nearby electronic equipment, such as radio receivers. It is the result of consistent effort of many amateurs and organizations who provided numerous cases of interferences. Thanks to them.

2. Another subject on issue is the Large LED Display Unit which has no EMC standard that suits well to existing standards. CISPR 11, CISPR 16, CISPR 22, CENELEC 210 and others are applicable here and there but not perfect. Among some of the deficiencies of existing standards, antenna tilting for the emission measurement should be considered for the correct measurement.

Therefore generating a new Generic Standard for large EUT is in progress under the Sub-committee H/WG4. The outcomes can be a new IEC-61000-6-7.

3. RFID(Radio Frequency Identification), TPMS(Tire Pressure Measurement System), RKE(Remote Keyless Entry) and similar automobile related devices (433.92 MHz) are also issues on possible interferences to amateur radio band. However, these subjects are seldom discussed in CISPR meetings.

The next CISPR meeting is scheduled to be held at Stockholm, Sweden, from September 11th  to 20th  2006. And the 70th IEC General Meeting is scheduled to be held in Berlin, Germany, from September 25 to 29, 2006

For whom who are interested in EMC matters, the following web site is recommended. http://www.iec.ch/zone/emc/ , http://www.iec.ch/cgi-bin/procgi.pl/www/iecwww.p?wwwlang=E&wwwprog=seabox1.p&seabox1=CISPR

Remarks :

CISPR : International Special Committee on  Radio Interference

Comite International Special des Perturbations Radioelectrique  was established in 1934 by a group of international organizations to address radio interference. 

CISPR is a non-governmental group composed of National Committees 
of the International Electrotechnical Commission (IEC), as well as numerous international organizations

May 30, 2006

Joong Geun Rhee, HL1AQQ, EMC Coordinator, IARU Region 3

____________________