BAND PLANS

IARU REGION 3

Introductory Notes

The IARU Region 3 Band Plans are revised at the triennial IARU Region 3 Conferences.

This version was adopted at the IARU R3 15th Conference, Ho Chi Minh City, Viet Nam 2012.

Basic Principles

The Basic Principles underlying the IARU Region 3 Band Plans are:

(1) In all cases of conflict between a band plan and the national regulations of a country, the latter shall prevail.

(2) Nothing in these band plans shall be construed as prohibiting different national arrangements, provided that harmful interference is not caused to stations in countries operating in accordance with the regional band plan.

(3) Notwithstanding item (2) above, Member Societies of IARU Region 3 are strongly urged to use these regional band plans as a basis for their national band plans.

Legends

The “Legends”/ “Abbreviations” used are:

CoA:	Emergency “Centre of Activity” frequency (IARU recommended)

EME:	Earth-Moon-Earth, Meteor Scatter, Auroral Scatter and other weak-signal modes

NB:	Narrow band modes including CW, RTTY, Packet and modes with similar bandwidth not exceeding 2 kHz.

Phone:	Phone operation includes SSTV, FAX and modes with similar bandwidth not exceeding 6 kHz.

Satellite:	This segment should be kept clear of other operating modes.

Secondary:	At 7.2 to 7.3 MHz, amateur stations shall not cause harmful interference to stations of the Broadcasting Service.

WB:	Wide band modes including FM.

Individual Band Plans

135 KHz

1.8 MHz

3.5 MHz

Note:

- Where the total band available nationally is 100 kHz or less, phone operation
may commence at 3.525 MHz.

- Emergency CoA frequency 3.600 MHz (All Modes ± 5 KHz )

7 MHz

Co primary

Note: Emergency CoA frequency 7.110 MHz (All Modes ± 5 kHz)

10 MHz

14 MHz

Note:

- Considering the dramatic increase in data mode usage on the 20 meter band, it is recommended that the sub-band for these classes of signals be 14.070 MHz to 14.112 MHz (with +/- 500 Hz at 14.100 MHz for beacons), and within that data sub-band the current practices of traditional data modes may continue up to 14.095 MHz with 14.095 to 14.112 MHz being reserved for other data modes including Packet.

- Emergency CoA frequency 14.300 MHz (All Modes ± 5 kHz)

18 MHz

Note: Emergency CoA frequency 18.160 MHz (All Modes ± 5 kHz)

21 MHz

Note: Emergency CoA frequency 21.360 MHz (All Modes ± 5 kHz)

24 MHz

28 MHz

50 MHz

144 MHz

430 MHz

1,240 MHz

Bands above 1300 MHz:

Societies should consult with the amateur satellite community for proposed satellite operating frequencies before deciding local band plans above 1300 MHz.

----------------------------------------------------

# Text boxes

CW / NB

Secondary

137.8 kHz

135.7 kHz

479 kHz

472 kHz

Secondary

CW & NB

CW

Phone Operation

1.834

1.830

2.0

1.8

1.840

RTTY

DX

3.510

3.9

3.5

CW

Phone Operation

3.600

CoA

3.775

3.800

3.535

Phone

DX

CW

DX

Phone Operation

NB

NB

7.110

CoA

7.2

Secondary

7.1

7.040

7.025

7.030

7.3

CW

7.0

CW

10.14

NB

Secondary

10.157.3

10.10

14.0

CW

Phone Operation

NB

NB

14.070

14.1127.040

14.23

( 5 kHz
is recommended
for SSTV

14.35

14.300

CoA

14.1

International Beacon

( 500 Hz
guard band
for beacons

CW

Phone

NB

18.100

18.168

18.068

18.160

CoA

18.110

International Beacon
( 500 Hz
guard band
for beacons

NB

21.0

21.45

CW

Phone Operation

21.34

( 5 kHz
is recommended
for SSTV

21.070

21.12540

21.15

International Beacon

( 500 Hz
guard band
for beacons

21.360

CoA

Phone

24.89

CW

NB

24.920

24.99

24.930

International Beacon
( 500 Hz
guard band
for beacons

29.7

CW

Beacons

Phone Operation

NB

Satellite

WB

28.190

28.3

28.150

28.050

29.3

28.68 ( 5 kHz
is recommended
for SSTV

29.510

28.0

28.2

International
Beacon
( 500 Hz
guard band
for beacons

CW

Beacons

WB

Phone and NB

50.5

50.1

54

50

Satellite

EME

144.035

144

148

146

145.8

Secondary

430

Satellite

EME

438

432.240

435

431.9

450

1,260

1,270

Satellite

1,296

1,297

EME

1,240

1,3000